## Slide 1
ELECTRONIC DIFFERENTIAL FOR ELECTRIC VEHICLES
RV College of
Engineering
Go, change the world
DTL Phase I Presentation
Chetan
Mallikarjun A L
Karthik P Shetty
Channaveeragouda MP
Mentor : Anusha A L
Designation : Associate Professor
Department of Electronics and Communication Engineering
*
Department of ECE
1
1RV21EC050
1RV21EC091
1RV21EC077
1RV21EC048

## Slide 2: Go, change the world
RV College of
Engineering
*
Department of ECE
2
EMPATHY PHASE

## Slide 3: Go, change the world
RV College of
Engineering
*
Department of ECE
3
Introduction
An Electronic Differential, also known as an electronic limited-slip differential (e-LSD) or electronic differential control, is an advanced automotive technology designed to optimize the distribution of torque (rotational force) between a vehicle's wheels, particularly in situations where traction might be compromised. Unlike traditional mechanical differentials, which use purely mechanical components to manage torque distribution, electronic differentials integrate sensors, computers, and actuators to achieve more precise control over wheel spin and power delivery.

## Slide 4: Go, change the world
RV College of
Engineering
*
Department of ECE
4
Advantages
of E-differential
over mechanical differential
Enhanced Traction Control
Precise Torque Distribution
Dynamic Adaptability
Reduced Understeer and Oversteer
Customizable Driving Modes
Compatibility with ADAS
Optimized EV Performance

## Slide 5: Go, change the world
RV College of
Engineering
*
Department of ECE
5
People’s responses and suggestions on our project

## Slide 6: Go, change the world
RV College of
Engineering
*
Department of ECE
6

## Slide 7: Go, change the world
RV College of
Engineering
*
Department of ECE
7

## Slide 8: Go, change the world
RV College of
Engineering
*
Department of ECE
8

## Slide 9: Go, change the world
RV College of
Engineering
*
Department of ECE
9
Suggestions
If my suggestion is actually read, I would be very much interested in contributing to this development. I don't know the means to reach out to you but if you can connect with me through the mail I am pretty much interested in understanding the problems and contributing to find a solution as well. My suggestion would be mostly wasteful until you text me back what are the issues you are facing currently.
Making use of e-diff for carbwalk like hummer or sliding motion which could help in easy turning in ghats and sliding on off road vehicles which could help to avoid obsticals just by sliding left or right instead of taking back and struggling to turn . This could also reduce the turning radius of even bigger vehicles .proper optimisation of e diff could help in easy overtaking and use e- diff for braking

## Slide 10: Go, change the world
RV College of
Engineering
*
Department of ECE
10
Guidance from FSAE experts

## Slide 11: Go, change the world
RV College of
Engineering
*
Department of ECE
11

## Slide 12: Go, change the world
RV College of
Engineering
*
Department of ECE
12
DEFINE PHASE

## Slide 13: Go, change the world
RV College of
Engineering
*
Department of ECE
13
“Design an electronic differential system to optimize torque distribution between the wheels of a vehicle, enhancing stability and control during turns.”

## Slide 14: Go, change the world
Objectives
Derive equations for the angular velocity: The equations for angular velocity is derived based on the concept of centripetal force. The equations represent angular velocity in terms of throttle and steering angle along with physical parameter of vehicle.
Mathematical Modelling: Develop a SIMULINK model for the derived equations and simulate the output i.e the speed of each motor at different throttle and steering angle.
Develop Final Model: The final model consists of a virtual steering and throttle using Arduino cloud to control the physical model of an E-vehicle. Wheel Encoders are used to verify the speed of each wheel.
RV College of
Engineering
*
Department of ECE
14

## Slide 15: Go, change the world
Using an electronic differential in electric vehicles (EVs) instead of a traditional mechanical differential can offer several benefits to Society
Drivers and Vehicle Owners:
i. Improved Performance
ii. Enhanced Safety
iii. Customizable Driving Modes
q Automotive Manufacturers:
i. Technological Leadership
ii. Brand value
Environmental Impact:
i. Efficient Power Distribution
ii. Reduced Tire Wear
RV College of
Engineering
*
Department of ECE
15

## Slide 16: Go, change the world
RV College of
Engineering
*
Department of ECE
16
Growth of Electrical Vehicles in India
Fig.1 Growth of Electrical Vehicles in India Financial Year-2022

## Slide 17: Go, change the world
RV College of
Engineering
*
Department of ECE
17
IDEATION PHASE

## Slide 18: Go, change the world
RV College of
Engineering
*
Department of ECE
18
IDEATION:
To develop an e-differential model that plays key role in delivering necessary angular velocity to different wheels.
The aim is to replace bulky mechanical differentials and provide faster turning mechanism in vehicles
Along with which reduce the power consumption as E-Diff use low power microcontrollers.
This phase is the journey through the simulation work along with the progress in hardware department.
Fig.2 Mechanical Differential
Fig.3 Electronic Differential

## Slide 19: Go, change the world
RV College of
Engineering
*
Department of ECE
19
The following equations are used to calculate the angular velocity to be given to the Wheels based on steering angle
ωl=ωv(1+d/2l * tan(ϴ))
ωr=ωv(1-d/2l * tan(ϴ))
ωl , ωr - Angular velocity of left and right wheel respectively
ωl - Throttle
d – Distance between two rear wheels
l – Distance between front and rear wheel
Fig.4 Steering Angle

## Slide 20: Go, change the world
RV College of
Engineering
*
Department of ECE
20
MATLAB simulation model:
SIMULINK MODEL FOR LEFT AND RIGHT WHEEL CONTROL
Fig.5 Simulink model for left wheel control
Fig.6 Simulink model for Right wheel control

## Slide 21: Go, change the world
RV College of
Engineering
*
21
FINAL SIMULINK MODEL
Fig.7 Simulink model for E-differential

## Slide 22: Go, change the world
RV College of
Engineering
*
22
CONTROL UNIT
LEFT MOTOR
RIGHT MOTOR
ωl=ωv(1+d/2l * tan(ϴ))
ωr=ωv(1-d/2l * tan(ϴ))
STEERING ANGLE
WHEEL ENCODER
WHEEL ENCODER
THROTTLE
ARDUINO IOT CLOUD
Fig.7 Block diagram for proposed model

## Slide 23: Go, change the world
Encoders : used in wheels, often referred to as "wheel encoders" or "rotary wheel encoders," are devices that measure the rotational motion and position of a wheel
MOTOR DRIVER: The L298 is a dual full-bridge motor driver integrated circuit (IC) commonly used to control the speed and direction of DC motors and stepper motors in robotics and automation applications.
RV College of
Engineering
*
Department of ECE
23
Fig.8 Encoders
Fig.9 Motor driver

## Slide 24: Go, change the world
CHARGING MODULE : The TP4056 charging module is a compact device that charges lithium-ion or lithium-polymer batteries efficiently and safely, with features like constant current and voltage charging, protection against overcharging, and LED indicators for charging status.
Li-ION BATTERY: The 18650 lithium-ion battery is a cylindrical cell format often used in various electronic devices, including laptops and power banks. Its specifications typically include a nominal voltage of 3.7V, capacity ranging from around 1500mAh to over 3500mAh, and a rechargeable design
RV College of
Engineering
*
Department of ECE
24
Fig.10 Charging module
Fig.11 Li-ion battery

## Slide 25: Go, change the world
ESP8266 :The ESP8266 is a Wi-Fi-enabled microcontroller module used for IoT and embedded applications. It enables wireless communication, sensor integration, web server hosting, and IoT device control.
DC MOTOR :A DC geared motor is a combination of a DC motor and a gearbox, providing controlled torque and speed output. It's used in various applications like robotics and automation to convert electrical energy into mechanical motion with adjustable speed and power.
RV College of
Engineering
*
Department of ECE
25
Fig.13 DC Motor
Fig.12 ESP8266

## Slide 26: Go, change the world
RV College of
Engineering
*
Department of ECE
26
Using Arduino Cloud Platform To Control signal
Fig.14 Arduino Cloud Platform To Control signal

## Slide 27: Go, change the world
RV College of
Engineering
*
Department of ECE
27
PROTOTYPE

## Slide 28: Go, change the world
RV College of
Engineering
*
Department of ECE
28
Fig.15 Wiring diagram

## Slide 29: Go, change the world
RV College of
Engineering
*
Department of ECE
29

## Slide 30: Go, change the world
RV College of
Engineering
*
Department of ECE
30
Fig.16 Dashboard interface of Arduino cloud

## Slide 31: Go, change the world
RV College of
Engineering
*
Department of ECE
31
Fig.17 Left motor speed

## Slide 32: Go, change the world
RV College of
Engineering
*
Department of ECE
32
Fig.18 Right motor speed

## Slide 33: Go, change the world
Thank You
RV College of
Engineering
*
Department of ECE
33